Robotics Series 5

Exercise 1: Camera Measurements
We took different measures under different circumstances. Mainly there are three experiment	setups that we used: different distances under dim light and a right angle, different distances	under good lighting and a right angle and different angles under good lighting and a fixed	distance. It could be noted that lighting mattered less than angle. We repeated one setup with	a different e-puck and a difference could be noted, although not too significant.

Exercise 2: Color recognition
In this exercise the e-puck should give a visual feedback about which color he sees:
1 led → red, 2 leds → blue, 3 leds → green
call math.stat(cam.red, minRed, maxRed, meanRed)
To calculate meanRed, meanBlue, meanGreen we used the code from the demo presented in	the lecture.

onevent ir_sensors
[...]
elseif color == RED then
leds[4] = 1
leds[2] = 0
leds[6] = 0
[…]
end
The e-puck has a variable color which is set to the corresponding color that he sees. He	compares this value to the constants RED, BLUE, GREEN and NO_COLOR and reacts	accordingly. We chose to light the leds 2,4,6 as signals. Led 4 is the one on the back of the	e-puck and leds 2 and 6 are at the sides. If the color is RED he lights leds[4], if color is	BLUE he lights the ones on the side and if it is GREEN all three leds are lit.

if meanRed > 24 and meanBlue < 23 and meanGreen < 23 then
color = RED
elseif meanRed < 22 and meanBlue > 19 and meanGreen < 22 then
color = BLUE
elseif meanRed < 20 and meanBlue < 20 and meanGreen > 16 then
color = GREEN
else
color = NO_COLOR
end
The interesting part was to calculate which color he saw. It is not enough to just check which	of the three mean values (meanRed, meanBlue, meanGreen) is the highest but one has to	take into account the ratio they have to each other. For that we tried using the measurements	of exercise 1 but we still had to make some adjustments. We did the measurements on an	other day than this exercise so that may be a reason. Because of course, it was impossible to	recreate exactly the same conditions as when taking the measurements. These ranges of	when to set the color to RED, BLUE or GREEN were determined by experimenting. We	started with our measured values and then kept changing them to get a better result. It is still	far from perfect, as it sometimes does not see the color it is supposed to or signals colors	when it should not.

Exercise 3: Color recognition – Explorer
This exercise is an extension of the previous exercise. Here, the e-puck drives around with	the EXPLORER behavior and simultaneously gives a visual feedback about the colors he	sees. To implement the behavior we used the code from series 3. We would have liked to test	other methods of recognizing colors but sadly we did not have enough time left to do that	since the measurements took much longer than anticipated. Of course, the color recognition	is much easier when the e-puck is standing still so during the implementation of this	exercise we also had to tweak the values for the calculation of the color. For example in our	calculation he was much too slow to recognize the colors and when driving he often did	not	show the correct color. By lowering the bounds he signaled colors sooner but this also	increases the rate of incorrect signals. With the bounds as they are now, he is much more	likely to signal a wrong signal but he is now fast enough to signal the colors when driving	around. In the simulation there are no leds so I had to come up with a different method of	signaling colors. The system I came up with works like this: e-puck 1 drives around and	explores. When he recognizes a color he emits a command with the color as the argument.	E-puck 3 reacts to those events by making a certain movement. If the argument he receives	is RED he drives forward, similarly if he receives BLUE/GREEN he starts turning right/left.	Whenever e-puck 1 sees none of these colors e-puck 3 receives NO_COLOR as an	argument. He then stops moving.

if avgRed > 6 and avgBlue < 4 and avgGreen < 4 then
color = RED
elseif avgRed < 4 and avgBlue > 6 and avgGreen < 4 then
color = BLUE
elseif avgRed < 4 and avgBlue < 4 and avgGreen > 6 then
color = GREEN
else
color = NO_COLOR
end
The values are also very different in the simulation as opposed to the physical arena. As was	explained in the lecture, in the simulator the e-puck sees the colors differently than in reality.	Each value in each camera array is either 0 or 100. So of course the boundaries to decide	which color he is seeing is different. In the simulation I also used a different method to	calculate the color values. Here used calculation of the average of all cameras from the	demo. With this method the average is always between 0 and 10 so the boundaries have to	be adjusted accordingly.

Note: for the measurements please view the file “05_13_GuertlerF_e_camvalues.pdf”